REMOTE measurement (one can notice the EXACT, REAL, resistor values – the generic resistor values, e.g. 1K, 10K 100K etc. were considered only in the VIRTUAL measurement) of Voltage- or Current- Controlled Alternative Voltage or Current Sources:

Voltage-Controlled Voltage Source (low gain):

Current-Controlled Voltage Source (low gain):

Voltage-Controlled A.C. Source

Voltage-Controlled A.C. Source

-one can notice the blue vcollector waveform: to the right, the flat area of BJT blocking and, to the left, the BJT saturation area where vcollector is almost coincident with vemitter  (and the distance between the red vemitter   waveform and the yellow vbase   waveform, representing uEB , is obviously greater!)

Checking the excellent resolution of the DAC:

10V / ( 212 ) = 0.00244140625 V

One can notice the difference between

(output noise is visible)

and

The peak voltage at the output is theoretically

0.002442V * ( 1 + 100K / 1K ) = 0.246642V

"What you see is what you get":     (

# Text boxes

Relay bench switching between MEDC and ECIR test boards

MEDC test board

ECIR test board

Relay bench for reconfiguration and ADC & DAC channels routing and ECIR test boards

Connection board

for DAQ

NI AT-MIO16E10